## Slide 1
AI-POWERED SURFACE DEFECT DETECTION — JINDAL STAINLESS
Smart Manufacturing & Quality Assurance | Slide 1: Business Context & High-Accuracy Architecture
Team: GenCoders
Lipi Bagarti & Kartik Ranjan Singh
1. Business Context & Strategic Imperative
Surface quality is the paramount metric in stainless steel manufacturing. Intelligent CV inspection directly advances Jindal Stainless's digital transformation by cutting scrap, reducing operational losses, and boosting customer trust in high-end austenitic/ferritic grades.
2. Background: Manufacturing Bottleneck
• Late Defect Detection: Scratches, scale, roll marks & edge cracks detected late cause yield loss, costly rework & customer rejections.
• Manual Inspection Limits: Human visual checks are slow, subjective, and physically impossible to sustain at 15–20 m/s line speeds.
3. GenCoders High-Accuracy Two-Tier Ensemble
• Tier 1 Multi-Model Detectors: YOLOv8s (Speed) + Faster R-CNN ResNet50 (Anchor Precision) + RT-DETR (Global Vision Transformer).
• Weighted Boxes Fusion (WBF): Replaces simple NMS with consensus spatial fusion & Multi-Model Agreement scoring (1, 2, or 3 models).
• Tier 2 Fine Texture Verifier: EfficientNet-B0 trained on 3,332 ground-truth crops to eliminate glare & surface oil false alarms.
• Dual-Confidence Fusion: Final Conf = 0.60 * Detector_Conf + 0.40 * Classifier_Conf.
4. Direct Fulfillment of 5 Key Considerations
Key Consideration | Required Spec | GenCoders Implementation
1. Accuracy & False Alarms | High mAP, Min False Stops | 82.4% mAP50, 68.5% False Alarm Drop
2. Multiple Defect Types | 6+ Stainless Defect Classes | Full coverage: Scratches, Scale, Crazing, etc.
3. Real-Time Mill Speed | 15–20 m/s (<20 ms latency) | 65+ FPS (15.4 ms) via TensorRT/ONNX
4. Usable Demo Interface | Image upload + visual flags | Streamlit Dashboard + Bounding Boxes + PLC
5. Cross-Grade Scaling | 200/300/400 Stainless Alloys | Active Learning & Domain Adaptation Loop
⚡ Real-Time Decision Engine & False Alarm Elimination:
• 5-Stage Gate: Confidence Gate ➔ Defect Area Filter ➔ Strip ROI ➔ Multi-Frame Tracker ➔ Severity Matrix. • Dual Verification: Every candidate bounding box is independently cross-verified by EfficientNet-B0 texture verifier before triggering plant actions.

## Slide 2
INDUSTRIAL DEPLOYMENT, PLC INTEGRATION & JINDAL ROADMAP
Slide 2: Action Item Deliverables, PLC/SCADA Automation, Financial ROI & Factory Scaling
Team: GenCoders
Lipi Bagarti & Kartik Ranjan Singh
1. PLC / OPC-UA Automation & Closed-Loop Actuation
• OPC-UA / Industrial Ethernet: Sub-20ms JSON telemetry sent directly to Siemens S7-1500 / Rockwell PLCs.
• Closed-Loop Actuation Rules: Structured severity-driven actions:
• • Low Severity: Logged silently in SQL database for coil surface quality heatmaps.
• • Medium Severity: Triggers audio-visual warning on operator Streamlit/SCADA HMI.
• • High / Critical Severity: Activates spray paint defect marker & mill deceleration trigger.
• Edge Compute Hardware Rig: Dual Line-Scan Cameras + High-Freq LED Strobes + NVIDIA Jetson AGX Orin / RTX 4000 GPU.
2. Path to Scaling Across Stainless Grades & Products
• Active Learning Loop: Borderline predictions (conf 0.40–0.60) flagged for metallurgical review and continuous retraining.
• Domain Transfer Pipeline: Pre-configured transfer learning from NEU-DET to Jindal 200/300/400 austenitic, ferritic & duplex stainless grades.
3. Projected Business Impact for Jindal Stainless
4. Action Plan for Production Deployment
• Phase 1 (Completed): Multi-model ensemble, WBF, crop dataset, decision engine, FastAPI backend, SQLite repository, Streamlit HMI demo.
• Phase 2 (Next Step): Hardware-in-the-loop OPC-UA PLC integration & transfer learning on live Jindal plant coil imagery.
₹4.2 Cr+
Annual Scrap & Downgrade Savings / Line
99.2%
Defective Coil Escape Prevention
< 4.5 Mo
Estimated Capital Payback Period
100%
Coil Traceability & SQL Database Logging